## Slide 1
Network Software Development
(Програмне забезпечення мереж передачі даних)
National Technical University of Ukraine “Igor Sikorsky Kyiv Polytechnic Institute”
Національний технічний університет України “Київський політехнічний інститут імені Ігоря Сікорського”

## Slide 2: SCHEDULE, REQUIREMENTS AND DEADLINES
  18 Лекцій (тести перед атестаціями, проміжні тести) + макс. 35 балів
  3 Лабораторні роботи
                Терміни здачі:
                ЛР 1 – до першої атестації (+макс. 15 балів) – 14.03-26.03
                ЛР2 – до другої атестації (+макс. 15 балів) – 02.05-15.05
                ЛР3 – до залікового тижня (+макс. 15 балів) – 21.05
                ! Лабораторні роботи приймаються тільки у визначені терміни
  Залік (+макс. 20 балів)
    Допуск до заліку – мін. 60 балів за поточним контролем

## Slide 3: Lecture’s, Lab’s resources
  Презентації лекцій, тести, звіти
    https://jaguar.ccc.ipt.pt/moodle/
  Лабораторні роботи
    Amazon Web Services Academy
  Поточні бали
    Електронний кампус КПІ

## Slide 4: COURSE OVERVIEW
Data Networks Overview
Network Software Development

## Slide 5: Introduction to the Internet of Things
Internet of Things: Concept
Internet of Things: Case Study

## Slide 6
Internet of Things: Concept

## Slide 7: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 8: Internet of Things
Physical things
  Exist in the physical world and are capable of being sensed, actuated and connected.
  Examples: industrial robots, goods and electrical equipment.
Virtual things
  Exist in the information world and are capable of being stored, processed and accessed.
  Examples: Multimedia content, application software.
Source: Recommendation ITU-T Y.2060

## Slide 9: How does it look like?
9

## Slide 10: What is IoT?
Internet of Things (IoT) comprises things that have unique identities and are connected to the Internet
The focus on IoT is in the configuration, control and networking via the Internet of devices or “Things” that are traditionally not associated with the internet
  Eg: pump, utility meter, car engine
IoT is a new revolution in the capabilities of the endpoints that are connected to the internet
10

## Slide 11: IoT (Some Industry Definitions)
A network connecting (either wired or wireless) devices, or ‘things’, that is characterized by autonomous provisioning, management, and monitoring. The IoT is innately analytical and integrated (IDC)
IoT is the next evolution of the Internet, connecting the unconnected people, processes, data, and things in your business today (Cisco)
IoT devices as those capable of two-way data transmission (excluding passive sensors and RFID tags). It includes connections using multiple communication methods such as cellular, short range and others. (GSMA)
Sensors & actuators connected by networks to computing systems. These systems can monitor or manage the health and actions of connected objects and machines. Connected sensors can also monitor the natural world, people, and animal” (McKinsey)
11

## Slide 12: IoT Building Blocks
12

## Slide 13: IoT Interaction
13

## Slide 14: Wireless Sensor Network
14

## Slide 15
Wireless Sensor Networks are networks that consists of sensors (nodes) and base stations which are distributed in an ad hoc manner.
These sensors work with each other to sense some physical phenomenon and then the information gathered is processed to get relevant results.
Wireless sensor networks consists of protocols and algorithms with self-organizing capabilities.
15
Wireless Sensor Networks

## Slide 16: Wireless Sensor Networks
sensor
  A transducer
  converts physical phenomenon e.g. heat, light, motion, vibration, and sound into electrical signals
sensor node
  basic unit in sensor network
  contains on-board sensors, processor, memory, transceiver, and power supply
sensor network
  consists of a large number of sensor nodes
  nodes deployed either inside or very close to the sensed phenomenon
16

## Slide 17
Integrated
Applications
Information
Processing
Network
Infrastructure
Sensing and
Identification
IoT: 4 layer Model

## Slide 18
IoT: Reference Model
In IoT solutions supporting Fog Computing (FC) part of the application processing is executed directly at IoT objects and only when needed. More complex and resource-consuming tasks are transferred to higher level units (FC units) or directly to the cloud.
Notes: Edge computing is interchangeable with fog computing.
Examples: a smart phone is the edge between body things and cloud, a gateway in a smart home is the edge between home things and cloud, a micro data center and a cloudlet is the edge between a mobile device and cloud

## Slide 19: IoT design requirements
IoT Network | Impact on IoT Systems Design
Scale | Tens of thousand sensors in a given site; or millions distributed geographically More pressure on application architectures, network load, traffic types, security, non-standard usage pattern
Heterogeneous end-points | Vast array of sensors, actuators, and smart devices – IP or non-IP Diverse data rate exchange, form factor, computing and communication capabilities, legacy protocols
Low Capex and Opex requirement | May be deployed before activation, maybe or cannot-be accessed once deployed Low numbers of gateways Link budget: e.g: UL: 155 dB (or better), DL: Link budget: 153 dB (or better) Devices deliver services with little or no human control, difficult to correct mistakes, device management is key
Criticality of services | Human life critical (Healthcare), Critical infrastructure (Smart Grid) Stringent latency (10ms for SG) and reliability requirements, may challenge/exceed network capabilities of today
Intrusiveness | Things with explicit intent to better manage end-users (eHealth, Smart Grid) Issues of Privacy become major obstacles
Geography | Movement across borders Issues of numbering for unique identification
Source: ITU CoE training on BB networks planning, Bangkok, Sep 2017
19

## Slide 20: IoT network connectivity requirements
IoT Network | Impact on IoT Systems Design
Resource-constrained endpoints | Severely resource constrained (memory, compute) Cost motivation: compute/memory several orders of magnitude lower, limited remote SW update capability, light protocols, security
Low Power | Some end-point types may be mostly ‘sleeping’ and awakened when required Sensors cannot be easily connected to a power source Reduced interaction time between devices and applications (some regulations state duty cycle of no more than 1%) Idle mode most of the time (energy consumption of around 100 µW). Connected mode just for transmission (mA) < 100 MHz clock frequency Embedded memory of few Mb
Embedded | Smart civil infrastructure, building, devices inside human beings Sensors deployed in secure or hostile operating conditions, difficult to change without impacting system, Security
Longevity | Deployed for life typically, have to build-in device redundancy Very different lifetime expectancy, rate of equipment change in IoT business domains much lower than ICT Industry
High Sensitivity on reception | Gateways and end-devices with a high sensitivity around -150 dBm/-125 dBm with Bluetooth lower than -95 dBm in in cellular
Source: ITU CoE training on BB networks planning, Bangkok, Sep 2017
20

## Slide 21: IoT Evolution
21

## Slide 22: Machine-2-Machine vs Internet of Things
22

## Slide 23: IoT Architecture - I
23

## Slide 24: IoT Architecture -II
24

## Slide 25: IoT Architecture
25

## Slide 26
Internet of Things: Case Studies

## Slide 27: Application Areas
27

## Slide 28: Factors and indicators of smart characteristics
28

## Slide 29: IoT Application Domains -I
29

## Slide 30: IoT Application Domains -II
30

## Slide 31: IoT Application Domains -III
31

## Slide 32: IoT Use Cases
32

## Slide 33: Intelligent Transportation
33
Evolution of transport applications and transport data assets

## Slide 34: Connected and Autonomous Vehicles
34

## Slide 35: Means of Automation
35

## Slide 36: Sensors and Subsystems
36

## Slide 37
Application Landscape - I
Information Services
  Fault prediction and response
  Data collection and generation
  Data dissemination and distribution
  Efficiency improvement
  Convenience services
Group Motion Control
  Platooning
  Intersection control
Probe Vehicle Data
  Vehicle Data Collection
  Event Data Collection
Safety Services
  Collision avoidance
  Hazard reporting
  Driver monitoring
Individual Motion Control
Signalized Intersections
  Traffic Light Prioritisation
  Signal Phase and Timing Information
  Green Light Optimal Speed Advisory
  Emergency Vehicle Priority
  Public Transport Priority
37

## Slide 38
Application Landscape - II
In-Vehicle Signage
  Dynamic Speed Limit Information
  Embedded VMS „Free Text“
  Dynamic Lane Management
  Shock Wave Damping
  Other Signage Information
Hazardous Location Notification
  Accident Zone
  Traffic Jam Ahead
  Weather Condition
  Warning Temporarily slippery road
  Animal or person on the road
  Obstacle on the road
  Emergency Vehicle Approaching/Intervention
  Railway Level Crossing
  Unsecured Blockage of a Road
  Alert Wrong Way Driving
  Public Transport Vehicle Crossing/At a Stop
Road Works Warning
  Lane closure (and other restrictions)
  Road closure
  Road Works – Mobile
  Winter Maintenance
  Road Operator Vehicle in Intervention/Approaching
38

## Slide 39
Awareness Driving
The exchange of status data via cooperative V2X communication, e. g. the position, speed, driving direction or special incidents like a vehicle defect, enables a set of information and warning services.
Examples are:
  Intersection Collision Warning
  Emergency Vehicle Warning
  Dangerous Situation Warning
  Stationary Vehicle Warning
  Traffic Jam warning
  Pre-/Postcrash Warning
*Source: https://car-2-car.org
39

## Slide 40
Sensing Driving
On top of status data, cooperative V2X capable road users can share observations gained by sensors, and advanced environmental information. This way, other traffic participants are not only warned against dangers they cannot perceive themselves yet; also, non-communicating road users are taken into account and protected in different traffic situations.
Examples are:
  Overtaking Warning
  Extended Intersection Collision Warning
  Vulnerable Road User Warning
  Cooperative Adaptive Cruise Control
  Long-term Road Works Warning
  Special Vehicle Prioritization
*Source: https://car-2-car.org
40

## Slide 41
Cooperative Driving
In addition to status and sensor data, cooperative V2X road users can also provide intention data, allowing them to interact intelligently and to coordinate their behaviour even in complex traffic situations. The prediction of expected behaviour of all road users is an important requirement for the long-term goal of highly automated and autonomous driving.
Examples are:
  (Static or dynamic) Platooning
  Area reservation
  Cooperative Merging
  Cooperative Lane Change
  Cooperative Overtaking
*Source: https://car-2-car.org
41

## Slide 42
Connectivity - I
42
Vehicle-to-Vehicle (V2V)
Vehicle-to-Infrastructure (V2I)
Vehicle-to-Pedestrian (V2P)
Vehicle-to-Network (V2N)
Vehicle-to-Broadband (V2B)
Vehicle-to-Cloud (V2C)
Vehicle-to-Device (V2D)
…
Vehicle-to-Everything (V2X)

## Slide 43
Connectivity
43

## Slide 44
Case Study Scenario
44

## Slide 45: Track Convoys
45

## Slide 46: Intelligent Public Transport Operations
46

## Slide 47: Intelligent Public Transport Operations
47

## Slide 48: Smart Cities
48

## Slide 49: Smart Cities
49

## Slide 50: Implementation of the Smart Cities
50

## Slide 51: Education
51

## Slide 52: Productivity
52

## Slide 53: Smart Home
53

## Slide 54: Smart Home
54

## Slide 55: Smart Home
55

## Slide 56: Structural Health Monitoring
56

## Slide 57: Healthcare and Remote Patient Monitoring
57

## Slide 58: Health Applications
58

## Slide 59: Medical application
Intel deployed a 130-node network to monitor the activity of residents in an elder care facility.
Patient data is acquired with wearable sensing nodes (the “watch”)
• Vital sign monitoring
• Accident recognition
• Monitoring the elderly
59

## Slide 60: Industry Sector Categories
60

## Slide 61: IoTs and Industry 4.0
The Convergence of IT and OT
Information Technology (IT) supports connections to the internet along with related data and technology systems and is focused on the secure flow of data across and organization
Operational Technology (OT) monitors and controls devices and processes on physical operational systems (assembly lines, utility distribution networks, production facilities, roadway systems etc.
Typically, IT does not get involved with the production and logistics of OT environments
IoT & Standards-based protocols are helping IT and OT converge and drive new economic value streams
61

## Slide 62: IoT Ecosystem
62

## Slide 63: Applications of Wireless Sensor Networks
63

## Slide 64: Environmental Applications
Forest fire detection
Bio-complexity mapping of environment
Flood detection
Precision Agriculture
Air and water pollution
64

## Slide 65: Environment monitoring
Great Duck Island
150 sensing nodes deployed throughout the island relay data temperature, pressure, and humidity to a central device.
Data was made available on the Internet through a satellite link.
65

## Slide 66: Environment monitoring
Zebranet: a WSN to study the behavior of zebras
Special GPS-equipped collars were attached to zebras
• Data exchanged with peer-to-peer info swaps
• Coming across a few zebras gives access to the data
66

## Slide 67: Military Applications
Monitoring friendly forces, equipment, and ammunition
Battlefield surveillance
Reconnaissance of opposing forces and terrain
Targeting
Battle damage assessment
Nuclear, biological, and chemical attack detection
67

## Slide 68: Underwater Acoustic Sensor Networks
68

## Slide 69: Other Commercial Applications
Environmental control in office buildings
Interactive museums
Detecting and monitoring car thefts
Managing inventory control
Vehicle tracking and detection
69

## Slide 70
Additional Info

## Slide 71: IoT Components
71

## Slide 72: IoT Definition
72

## Slide 73: IoT Basic Characteristics -I
73

## Slide 74: IoT Basic Characteristics -II
74